## Slide 1: Slot floor monitoring
Chapter 3

## Slide 2: Outline
Overview of MCS
A. Status and events from common hardware devices
B. EGM disable mechanism
C. Event subscription and report
D. Connection monitoring and event buffering

## Slide 3: Objectives
At the end of this chapter, you should understand
  How the host learns the structure and capability of an EGM in the EGM restart sequence,
  How local events affect EGM device status and fire events to notify the host,
  How devices affect the overall state of the EGM,
  How to diagnose causes of disabling or locking the EGM,
  How event subscription enables the host to get an up-to-date model of the state of the EGM, and
  How communication problems are detected and handled by the EGM.

## Slide 4: Online monitoring and control
An online monitoring and control system (MCS) is a game management system that continuously monitors each EGM in a gaming floor
  Logging, searching and reporting of significant events
  Collection of individual device financial and meter data
  Reconciliation of meter data against hard and soft counts
  … from GLI standard 13

## Slide 5: Event and meter reports
MCS performs its tasks mainly by subscribing to meter and event reports
  Slot machines periodically report current values of meters
  When something significant happens, slot machines send event reports to MCS immediately.
Monitoring and control system
Other host, e.g. progressive controller
54, 38

## Slide 6: Example: IGT visual slot performance
Monitor current status of slots in real-time
Report and log events from slots
For more info, ref to the manual "IGT Visual slot performance.pdf"

## Slide 7: More examples
IGT's sbX: http://www.igt.com/mo-en/systems/sbx.aspx
Bally's SMS: http://www.ballytech.com/Systems/Accounting/SMS
Aristocrat's OASIS 360: Surveillance Monitor™ and OmniVIEW™ http://www.aristocrat.com.au/products/systems/documents/oasis%20360%20overview%200710.pdf
Advansys Accounting & Cage: http://advansys.si/products/slotscanner/accounting-cage/

## Slide 8: Part A. Device states and events
How device state changes trigger events, and how occurrence of events are reflected by device states.

## Slide 9: Outline
Status of common hardware devices
  Cabinet, note acceptor, printer
Significant events
  From GLI to G2S
Device fires events when change in device status occurs
Host commands to enable / disable a device

## Slide 10: GLI-13 Significant events
GLI-13 requires an EGM to notify the slot floor monitoring system in the following cases:
  Power reset or power failure
  Low RAM battery power
  Door openings
  Reel spin errors
  Bill validator errors: stacker full, bill jam
  Printer errors: printer empty/ paper low, printer disconnect / failure
  Handpay condition (large win, progressive, cancel credit) (handpay locking in section B. more detail in later chapters.)

## Slide 11: Common hardware devices
This section studies status change, events and profile of three common hardware devices.
You’ll also see how G2S events satisfy the GLI-13 requirements on significant events.
Exercise: map GLI significant events to G2S events
cabinet
noteAcceptor
For host 1
communications
meters
eventHandler
printer
voucher
handpay
gamePlay
gamePlay

## Slide 12: Cabinet device
The cabinet device represents the physical housing of the EGM.
Maintain status and fire events for the following:
  Door open
  Service lamp
  Other cabinet faults

## Slide 13: Cabinet status
A host can retrieve the Cabinet status with getCabinetStatus / cabinetStatus.
cabinetStatus contains
  (EGM controlled) egmEnabled
  (Host controlled) hostEnabled, hostLocked, enableGamePlay, enableMoneyIn
  (Door status and lamp) cabinetDoorOpen, logicDoorOpen, auxDoorOpen, serviceLampOn
  (extension g2sA) generalFault, reelTilt, videoDisplayFault, nvStorageFault, generalMemoryFault
  Other attributes that aggregate the status of all devices (to be discussed in Section C)
When the status changes, host is notified by events

## Slide 14: Sample commands
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
logicDoorOpen="false" cabinetDoorOpen="false" ...
serviceLampOn="false"
g2sA:generalFault="false" g2sA:reelTilt="false"
g2sA:videoDisplayFault="false" g2sA: nvStorageFault="false"
g2sA:generalMemoryFault="false"
egmState="G2S_enabled" …
/> </cabinet>
<cabinet deviceId="1" sessionType="G2S_request" ... >
<getCabinetStatus />
</cabinet>
Aggregate status to be discussed

## Slide 15: Events and status updates
When a significant event happens, there is usually update in some status attributes.
  The EGM fires events when status attributes change. For example, if cabinet door is opened, CBE307 is fired, and the attribute cabinetDoorOpen = true. When the door is closed, CBE308 is fired, and the attribute cabinetDoorOpen=false.
In case of door open or cabinet fault, the EGM disables the cabinet device
  Set the status attribute egmEnabled=false
  Reset to egmEnabled=true when doors closed and all faults cleared.
Changes to egmEnabled fire events
  CBE001 Device Disabled by EGM
  CBE002 Device Not Disabled by EGM
'EGM disables' = device disabled by local fault

## Slide 16: Status changes and related events
Status attribute | Events
cabinetDoorOpen | CBE307 Cabinet door opened. CBE308 closed
logicDoorOpen | CBE303 Logic door opened. CBE304 closed
auxDoorOpen | CBE305 Auxiliary door opened. CBE306 closed
g2sA:generalFault g2sA:reelTilt | CBE309 General cabinet fault
g2sA:videoDisplayFault | CBE310 Video Display Error
g2sA:nvStorageFault | CBE311 Non-Volatile Storage Fault
g2sA:generalMemoryFault | CBE312 General Memory Fault
The above faults | CBE313 All Cabinet Faults Cleared
serviceLampOn | CBE301 Service lamp on. CBE302 off
--- | CBE323 Backup Battery Low
--- | CBE325 EGM Power Up/Restart
These four events do not affect egmEnabled…
Events in RED disables the device. Events in GREEN may enable the device.

## Slide 17: Doors in cabinet
Doors in G2S cabinet class are logical
  Logic door provides access to the main processor board, game chips or other components related to game determination
  Auxiliary door provides access to auxiliary storage area used to store cashbox or other items of value. (e.g. remove stacker, fill the hopper)
  Cabinet door provides access to other components
Opening a physical door may trigger >1 logical door open event.
In a real EGM, you may need to open aux door before opening the stacker door. (no implemented in RST)
Cabinet device has meters and status attributes that record the door open count and time of last open

## Slide 19: Note Acceptor device
A noteAcceptor device represents one note acceptor (i.e. bill validator) device.
Maintain status and fire events for the following:
  Stacker door open
  Stacker removed
  Stacker full
  Stacker jammed and fault
  Other device faults
Notes: http://jcmglobal.com/en/products/productdetails.aspx?ProdID=UBA

## Slide 20: Attributes in noteAcceptorStatus
A host can retrieve the noteAcceptor status with getNoteAcceptorStatus / noteAcceptorStatus.
noteAcceptorStatus contains
  doorOpen, stackerRemoved
  stackerNearlyFull, stackerFull
  stackerJam, stackerFault, acceptorJam, acceptorFault
  disconnected, illegalActivity
  firmwareFault, mechanicalFault, opticalFault, componentFault, nvMemoryFault
Change of these status attributes trigger events
noteAcceptorStatus also contains an attribute noteValueInEscrow for the value of note in escrow
Notice that stackerNearlyFull does not disable the note acceptor.

## Slide 21: Events and status updates
When some significant event happens, usually there is update in some status attributes.
  During drop process, the stacker is removed, then an empty stacker is inserted. The EGM fires NAE103 when stacker is removed, and sets the attribute stackerRemoved=true. After insertion of an empty stacker, the EGM fires NAE104 and sets the attribute stackerRemoved=false.
In case of stacker removed or other NA faults, the EGM disables the noteAcceptor device
  Set the status attribute egmEnabled=false
  Reset to egmEnabled=true when all faults cleared
Changes to egmEnabled fire events
  NAE001 Device Disabled by EGM
  NAE002 Device Not Disabled by EGM

## Slide 22: Status changes and related events
Status attribute | Events
doorOpen | NAE112 Stacker door opened. NAE113 closed
stackerRemoved | NAE103 Stacker removed. NAE104 Stacker inserted.
disconnected | NAE901 Device Disconnected. NAE902 connected.
stackerFull | NAE105 Stacker full
stackerJam | NAE106 Stacker jammed
stackerFault | NAE107 Stacker fault
acceptorJam | NAE101 Acceptor jammed
acceptorFault | NAE102 Acceptor fault
illegalActivity | NAE908 Illegal activity detected
… other faults | NAE903 – 907
The above faults | NAE099 All device faults cleared
stackerNearlyFull | NAE117 Stacker Nearly Full
NAE117 does not disables NA device.
Events in RED disables the device. Events in GREEN may enable the device.

## Slide 23: Printer device
A printer device represents one printer device, which prints voucher (i.e. ticket)
Maintain status and fire events for the following:
  Chassis or print head opened
  Paper jam or empty
  Paper low
  Other device faults
Notes: http://jcmglobal.com/en/products/productdetails.aspx?ProdID=PAYCHECK

## Slide 24: Attributes in printerStatus
A host can retrieve the printer status with getPrinterStatus / printerStatus.
printerStatus contains
  disconnected
  chassisOpen, printHeadOpen
  paperJam, paperEmpty
  paperLow
  illegalActivity
  firmwareFault, mechanicalFault, opticalFault, componentFault, nvMemoryFault
Change of these status attributes trigger events
Notice that paperLow does not disable the printer.

## Slide 25: Events and status updates
When some significant event happens, usually there is update in some status attributes.
  When the printer is out of paper, EGM fires PTE207 and sets the attribute paperEmpty=true. When operators replenish paper, EGM fires PTE099 and sets the attribute paperEmpty=false.
In case of paper empty or other PT faults, the EGM disables the printer device
  Set the status attribute egmEnabled=false
  Reset to egmEnabled=true when paper replenished and all faults cleared.
Changes to egmEnabled fire events
  PTE001 Device Disabled by EGM
  PTE002 Device Not Disabled by EGM

## Slide 26: Status changes and related events
Status attribute | Events
chassisOpen | PTE201 Printer chassis opened. PTE202 closed
printHeadOpen | PTE203 Print head opened. PTE204 closed.
disconnected | PTE901 Device Disconnected. PTE902 connected.
paperJam | PTE205 Paper Jam
paperEmpty | PTE207 Paper Empty
.. other faults | PTE903 – PTE907
illegalActivity | PTE908 Illegal Activity Detected
The above faults | PTE099 All device faults cleared
paperLow | PTE206 Paper Low
PTE206 does not disable PT device.
Events in RED disables the device. Events in GREEN may enable the device.

## Slide 27: Host disables a device
A host can send set[class]State enable=false to disable a device
  The device has status attribute hostEnabled:=false
  The device returns [class]Status to report current status
  the host can send set[class]State enable=true to re-enable the device
The device fires related events, e.g.
  CBE003, NAE003, PTE003 Device disabled by host
  CBE004, NAE004, PTE004 Device not disabled by host

## Slide 28: A device is disabled
A device is disabled if egmEnabled=false or hostEnabled=false
Limited device functions when disabled
  NA does not accept notes
  PT must not print any ticket
  CB does not start new games, stops all transaction, and does not accept cash in. It may cash out the player (ref. profile attribute g2s2:cashOutOnDisable §3.14.1.12)
Some device rejects some commands when disabled (refer to the Request-Response Pairs section in G2S spec)

## Slide 29: setCabinetState
setCabinetState supports finer control with the following attributes
  enableGamePlay – when false, EGM should cease all game play after current (base or bonus) game. Related events: CBE101, CBE102
  enableMoneyIn – when false, EGM should cease accepting money in. Related events: CBE103, CBE104
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true"
enableGamePlay="true" enableMoneyIn="false" … /> </cabinet>
<cabinet deviceId="1" sessionType="G2S_request" ... >
<setCabinetState enable="true"
enableGamePlay="true" enableMoneyIn="false" />
</cabinet>

## Slide 30: Lab 3-1
Experiment when different local events of the cabinet, note acceptor and printer device in SmartEGM.
Examine events and status changes for the following maintenance tasks
  Note drop
  Replenish paper for printer

## Slide 31: Part B. Disable mechanism
What affects the overall state of an EGM, and how to diagnose causes of disabling

## Slide 32: Outline
egmState – overall state of the EGM
  Online and playable, locked, disabled, others
  Local event / host commands?
  More than one device (incl. Cabinet) may disable / lock the EGM and forbid game play.
  Related events
Diagnose the causes that make an EGM non-playable

## Slide 33: Two aspects of the Cabinet device
The Cabinet class defines a single Cabinet device in EGM
The cabinet device represents the physical housing of EGM
  Status and events related to door open, power-off, etc.
The cabinet device also supports overall control of EGM
  Enable / disable, lock the EGM
  Commands to set date and time, reset EGM
  Profile information include currency, locale
  Meters: credit meters, wager, wins, etc
  Status attributes that reflect the aggregate state of all devices in the EGM

## Slide 34: More cabinetStatus attributes
cabinetStatus also contains the following attributes about the overall status of the whole EGM
  egmState: the overall state of the EGM
  When the EGM is disabled / locked, deviceClass and deviceId indicate the device causing the problem
  Otherwise, deviceClass and deviceId indicate the last game played
  Further info available in gamePlayId, themeId, paytableId, denomId, maxWagerCredits

## Slide 35: State of the EGM: egmState
The egmState attribute of the cabinetStatus reflects the aggregate state of all devices in the EGM.
  Enabled and playable: G2S_enabled
  Disabled: G2S_egmDisabled, G2S_hostDisabled, G2S_transportDisabled
  Locked: G2S_egmLocked, G2S_hostLocked
  Operator action: G2S_operatorDisabled, G2S_operatorMode G2S_operatorLocked, G2S_demoMode, G2S_auditMode
Possibly multiple devices are disabled / locked
  EGM becomes enabled only after all faults are cleared

## Slide 36: EGM is enabled and playable
An EGM is available for play only when egmState=enabled
  EGM is not locked
  EGM is not disabled
  EGM is not in any special mode (e.g. operator, audit …)
  When an EGM becomes ‘enabled and playable’, it generates event CBE205 EGM enabled and playable

## Slide 37: Operator actions at EGM
Operator actions at EGM may generate events and changes to egmState. They generally forbid game play.
egmState | Events
operatorDisabled | CBE202 EGM disabled – Operator menu
operatorMode | CBE206 Operator menu activated
demoMode | CBE207 Demo menu activated
auditMode | CBE208 Meters/Audit mode initiated
operatorLocked | CBE209 EGM locked – Operator menu

## Slide 38: Locking
  Locking freezes an EGM operation
  Following the completion of the current game cycle, EGM MUST NOT initiate any new games, accept any money in or dispense any money out (including transfers and vouchers).
Some device may lock the EGM in normal operation
  E.g. handpay condition in large win
  Set cabinet.egmState=egmLocked
  Generate CBE210 Device Action Locked EGM
A host may lock the EGM by sending the command set[class]LockOut
  Set cabinet.egmState=hostLocked
  Generate CBE211 Host Action Locked EGM

## Slide 39: egmLocked
Some device can lock the whole EGM.
  The most common case is handpay
  Lock possibly in the middle of a game
  egmLocked=true for the locking device
  In the cabinet status: egmState=egmLocked, deviceClass and deviceId indicate the locking device
gamePlay, commConfig optionConfig and download devices can also lock the EGM during configuration.
No events from the locking device

## Slide 40: Sample commands
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
egmState="G2S_egmLocked" deviceClass="G2S_handpay" deviceId="9" …
/> </cabinet>
<handpay deviceId="9" sessionType="G2S_response" ... >
<handpayStatus
egmEnabled="true" hostEnabled="true" egmLocked="true" /> </handpay>
<getCabinetStatus />
<getHandpayStatus />
Status of two devices in handpay condition.

## Slide 41: hostLocked
A host can lock the cabinet with setCabinetLockout
The cabinet device status attribute hostLocked=true
  In the cabinet status: egmState=hostLocked, deviceClass and deviceId indicate the locking device (i.e. the cabinet itself)
Generate events
  CBE009: Device Locked by Host
  CBE010: Device Not Locked by Host
In addition to cabinet, owner host of the following device may also lock an EGM
  progressive, bonus, voucher
  wat, mediaDisplay, smartCard, dft

## Slide 42: Sample commands
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true" hostLocked="true"
enableGamePlay="true" enableMoneyIn="true"
egmState="G2S_hostLocked" deviceClass="G2S_cabinet" deviceId="1" …
/> </cabinet>
<cabinet deviceId="1" sessionType="G2S_request" ... >
<setCabinetLockOut lockOut="true"/>
</cabinet>

## Slide 43: EGM is disabled
  EGM is enabled when all required device are enabled (egmEnabled=hostEnabled=true)
EGM is disabled when any required device is disabled or required transport is down
  egmState = G2S_hostDisabled or G2S_egmDisabled
  deviceClass, deviceId identify which device caused the disabled condition
EGM may also disabled if the transport is down
  egmState = G2S_transportDisabled
EGM disabling typically causes stopping game play (after complete current game) and cashing out the player
To discuss in Section E.

## Slide 44: EGM is egmDisabled
A required device is disabled by some faults
  The device has profile attribute requiredForPlay=true
  The device has status attribute egmEnabled=false
  The device fires related events (e.g. PTE207 Paper empty)
The cabinet device
  status attribute egmState=G2S_egmDisabled
  Fires CBE203 Device action disabled EGM

## Slide 45: Sample commands
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
egmState="G2S_egmDisabled" deviceClass="G2S_printer" deviceId="9" …
/> </cabinet>
<printer deviceId="9" sessionType="G2S_response" ... >
<printerStatus
egmEnabled="false" hostEnabled="true" paperEmpty="true" /> </printer>
<getCabinetStatus />
<getPrinterStatus />
Status of two devices in case of out-of-paper.

## Slide 46: Sample commands
<getCabinetStatus />
Status of the cabinet when a cabinet door is opened.
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="false" hostEnabled="true" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
logicDoorOpen="true" cabinetDoorOpen="false" ...
egmState="G2S_egmDisabled"
deviceClass="G2S_cabinet" deviceId="1” …
/> </cabinet>

## Slide 47: EGM is hostDisabled
A required device is disabled by some commands from host
  The device has profile attribute requiredForPlay=true
  The host sends set[class]State enable=false to the device
  The device has status attribute hostEnabled=false
  The device fires related events
The cabinet device
  status attribute egmState=G2S_hostDisabled
  Fires CBE204 Host action disabled EGM

## Slide 48: Sample commands
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="true" hostEnabled="true" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
egmState="G2S_hostDisabled" deviceClass="G2S_noteAcceptor" deviceId="7" … /> </cabinet>
<noteAcceptor deviceId="7" sessionType="G2S_response" ... >
<noteAcceptorStatus egmEnabled="true" hostEnabled="false" … /> </noteAcceptor>
<getCabinetStatus />
Status of two devices if the host disables the note acceptor
<noteAcceptor deviceId="7" sessionType="G2S_request" ... >
<setNoteAcceptorState enabled="false" … /> </noteAcceptor>

## Slide 49: Exercise
<cabinet deviceId="1" sessionType="G2S_response" ... >
<cabinetStatus
egmEnabled="???" hostEnabled="???" hostLocked="false"
enableGamePlay="true" enableMoneyIn="true"
egmState="???" deviceClass="???" deviceId="???" … /> </cabinet>
What is the cabinet status if the host disables it?
<cabinet deviceId="1" sessionType="G2S_request" ... >
<setCabinetState enabled="false" … /> </cabinet>

## Slide 50: Lab 3-2
Disable / lock the cabinet by commands
  Check egmState, deviceClass and deviceId. Which device disables/locks the EGM?
  Any player activity allowed?
Cabinet door open will disable the EGM.
  Observe the sequence of events (3 events at door open!)
  How cabinet status identifies the cause of disabled condition?
  Also check currency door open. And when two doors are open
Filter the Cabinet commands / events in startup sequence
Check the attributes enableMoneyIn and enableGamePlay in setCabinetState.

## Slide 51: Part C. Event Subscription and Report
Understand how the host subscribes to EGM events and the rich data that is included in event report messages

## Slide 52: Outline
eventHandler devices
Event and affected data
Event discovery
Event subscription
  Get, set, and clear event subscription list
Event reporting
  Message structure, affected data
  Request/Response, Notification

## Slide 53: What is an Event?
An unsolicited message sent by an EGM, triggered by the EGM or a host-initiated command
Events are associated with changes in device status, meters and transaction logs
Can be sent to multiple host
Coin in
Game play
Coin out
Configuration changed
Game enabled
Bonus award

## Slide 54: eventHandler class
eventHandler is a class designed to manage all aspects of events in the EGM
  Event discovery
  Manage event subscription lists
  Manage delivery of events
  Manage collection of associated data
Every host has its own event handler device
  deviceId = hostId

## Slide 55: Event Codes
Events are identified in each class by event codes, which consists of
  3-character GSA-assigned manufacturer identifier
  2-character class identifier
  Letter “E” indicating “Event”
  3-digit event number
Example: G2S_EHE001
Note: we generally omit the prefix ‘G2S_’ in course notes for brevity

## Slide 56: Event and Affected Device Data
Each G2S event is associated with changes in device status, meters, and/or transaction log entries.
  configurationId in status reflects changes in profile.
Any changes in these data also involve an event.
A host can maintain an up-to-date data model of EGM devices by subscribing to all related events.
  Note: an event in a class may affect data in another class
Class
Device
Status
Profile
Meters
Meters
Transaction logs
events

## Slide 57
These affected data set are documented in the event section at the end of each chapter on each G2S class. For example, read the table in G2S spec 6.24 "Event codes of gamePlay class".

## Slide 58: Data Sent with an Event Report
Device status for affected devices
  Full device status as returned by get[Class]Status command
  Reports status at the time event was placed on command queue. (NOT at the time of event occurrence)
Meters for affected devices
  May also include class level meters (with deviceId=0)
  The complete device meter set, OR only device meters that have changed as a result of the event
Initiating transaction log
  Only included as affected data if attributes within the transaction were updated.

## Slide 59: Sample Event Message
<eventHandler deviceId="1" sessionType="G2S_request" ... >
<eventReport deviceClass="G2S_cabinet" deviceId="1"
eventCode="G2S_CBE307" eventText="Cabinet Door Open"> <deviceList>
<statusInfo deviceClass="G2S_cabinet" deviceId="1">
<cabinetStatus egmEnabled="false"
cabinetDoorDateTime="..." ... />
</statusInfo>
</deviceList>
<meterList>
<meterInfo ...>
<deviceMeters deviceClass="G2S_cabinet" deviceId="1">
<simpleMeter meterName="G2S_cabinetDoorOpenCnt"
meterValue="12"/>
</deviceMeters>
</meterInfo>
</meterList>
</eventReport>
</eventHandler>
Changes in device status
Changes in device meters

## Slide 60: Discovering Events
The command getSupportedEvents allows a host to determine the events supported by devices in an EGM
  deviceClass (for all classes, G2S_all)
  deviceId (for all device, -1)
The EGM returns supportedEvents
  Which consists of >=0 supportedEvent elements, each containing the attributes deviceClass, deviceId, eventCode, eventText

## Slide 61: Sample commands
<eventHandler deviceId="1" sessionType="G2S_request" ... >
<getSupportedEvents deviceClass="G2S_cabinet" deviceId="-1" /> </eventHandler>
Event discovery, usually done in host startup algorithm
<eventHandler deviceId="1" sessionType="G2S_response" .... >
<supportedEvents> <supportedEvent deviceClass="G2S_cabinet" deviceId="1"
eventCode="G2S_CBE001"
eventText="EGM Disabled Cabinet"/>
<supportedEvent … />
<!-- more events supported by the device -->
</supportedEvents>
</eventHandler>

## Slide 62: Host subscriptions
A host can manage host subscription with eventHandler class commands
  Read the subscription: getEventSub / eventSubList
  Add to the subscriptions: setEventSub / setEventSubAck
  Clear a subscription: clearEventSub / clearEventSubAck
  Related event: EHE101 Event subscription changed
Event subscriptions are persisted
Note: in addition to host subscription, EGM may also have forced subscription, which is configured at EGM or set by manufacturer. This course will not cover forced subscription.
Subscribe events

## Slide 63: Subscribing to Events
A host subscribes to specific events with setEventSub / setEventSubAck
The subscription indicates what affected data to include in event reports:
  Device status, class meters, device meters, transaction log
  If an event subscription includes an event that already has a subscription, the new subscription is combined with the previous by applying 'OR' on the affected data.
The subscription also specify whether to persist the event
  EGM can resend a persisted event if it receives no ack from host.
A host can only subscribe to events for devices to which it is either an owner or a guest

## Slide 64: The setEventSub element
setEventSub has 1 or more eventHostSubscription element, which has the following attributes
  deviceClass: for all classes, use G2S_all
  deviceId: for all devices in the class, use -1
  eventCode: for all events in the device, use G2S_all
  sendDeviceStatus: send the affected device status?
  sendTransaction: send the affected transaction record?
  sendClassMeters: send the affected class level meters?
  sendDeviceMeters: send the affected device level meters?
  sendUpdatableMeters: send the complete set of meters (false) or only meters that were updated (true)
  eventPersist: saves this event in log to enable resend?
Affected data to send
Which events?

## Slide 65: Sample commands
<eventHandler deviceId="1" sessionType="G2S_request" ... >
<setEventSub>
<eventHostSubscription
deviceClass="G2S_cabinet" deviceId="-1" eventCode="-1"
sendDeviceStatus="true" sendTransaction="true"
sendClassMeters="false" sendDeviceMeters="true"
sendUpdatableMeters="false" eventPersist="false" /> <eventHostSubscription deviceClass="G2S_noteAcceptor" deviceId="-1"
eventCode="-1" sendDeviceStatus="true" />
</setEventSub>
</eventHandler>
Subscribe to all events of cabinet device, and send affected status, transaction log and device meters. Send complete set of device meters, but omit class meters.) Subscribe to all events of NA, but send only affected status.
<eventHandler deviceId="1" sessionType="G2S_response" .... >
<setEventSubAck/> </eventHandler>

## Slide 66: Clearing Event Subscriptions
A host clears a subscription to specific events with clearEventSub command
  EGM returns clearEventSubAck
clearEventSub has 1 or more eventSelect elements, which has the following attributes
  deviceClass
  deviceId
  eventCode
  (use the same value for wildcard as in setEventSub)

## Slide 67: Reading Event Subscriptions
The host can read the list of subscribed events with getEventSub command
  The EGM returns eventSubList
getEventSub has two attributes
  getForcedSubs: returns forced event subscriptions?
  getHostSubs: returns host event subscriptions?
getEventSub has 1 or more eventSelect sub-elements, which has the following attributes
  deviceClass, deviceId, eventCode
  (same as in clearEventSub)

## Slide 68: The eventSubList element
eventSubList has 1 or more eventSubscription element, which has the following attributes
  deviceClass, deviceId, eventCode, eventText: a specific event of a device
  sendDeviceStatus: send the affected device status?
  sendTransaction: send the affected transaction record?
  sendClassMeters: send the affected class level meters?
  sendDeviceMeters: send the affected device level meters?
  sendUpdatableMeters: send the complete set of meters (false) or only meters that were updated (true)
  eventPersist: does this event need to be persisted?
  Forced subscriptions are reported with similar attributes with name forced??? instead of send???

## Slide 69: Persisted vs. non-persisted event
When a host subscribes to an event, it can indicate the EGM to persist the event (attribute persistEvent)
Persisted event are …
  sent using eventReport as request. The host has to acknowledge with eventAck after processing the event
  added to event log of the eventHandler device. EGM track whether the host has acknowledged.
Non-persisted events are
  sent using eventReport as notification.
  not added to event log. EGM cannot track the event.
More about persisted events and event log in Section E.
Notes: The event log keeps track of whether the events are acknowledged. The EGM will retry sending commands for events not acknowledged by hosts.

## Slide 70
Subscriptions for the event?
Assign event ID
Persist event?
Add event details to event log
Gather associated data
Send to comms for delivery
Timeout waiting for Ack?
Event occurs
yes
Gather associated data
Send to comms for delivery
yes
yes
done
no
no
done
done
no
When event occurs, event is evaluated against each host subscription and added to the outbound command queue of communications device of the subscribing host
  The same event may be sent to several hosts
Persisted events are added to event log. EGM resends the event report if it timeout while waiting for ack.
Event reporting

## Slide 71: Request and response in persisted events
<eventHandler deviceId="1" sessionType="G2S_request" ... >
<eventReport
deviceClass="G2S_noteAcceptor" deviceId="1"
eventCode="G2S_NAE114" eventText="Note Accepted"
eventId="99” eventDateTime="..." transactionId="888”> <deviceList>...</deviceList>
<transactionList>...</transactionList>
<meterList>...</meterList>
</eventReport> </eventHandler>
<eventHandler deviceId="1" sessionType="G2S_response" ... >
<eventAck eventId="99" /> </eventHandler>
Host returns an acknowledgement after processing the event.

## Slide 72: Notification in non-persisted events
<eventHandler deviceId="1" sessionType="G2S_notification" ... >
<eventReport
deviceClass="G2S_noteAcceptor" deviceId="1"
eventCode="G2S_NAE114" eventText="Note Accepted"
eventId="99” eventDateTime="..." transactionId="888”> <deviceList>...</deviceList>
<transactionList>...</transactionList>
<meterList>...</meterList>
</eventReport> </eventHandler>
No application acknowledgement from host. EGM is not sure whether the host has processed the event.

## Slide 73: eventReport Element
eventReport has the following attributes:
  deviceClass, deviceId, eventCode, eventText
  eventId: unique identifier for a particular event. used to match events sent to several hosts
  eventDateTime: date and time that this event occurred
  transactionId: transaction identifier associated with event; 0 if no associated transaction
eventReport has three sub-elements to report affected associated data
  deviceList (0 or 1), transactionList (0 or 1), meterList (0 or 1)

## Slide 74: deviceList Element
deviceList contains 1 or more statusInfo element
  statusInfo has the attributes: deviceClass, deviceId
  statusInfo has 1 sub-element: [device status], which is the status element of the affected device. (i.e. the same element as the command [class]Status)
<eventReport ... transactionId="888">
<deviceList>
<statusInfo deviceClass="G2S_noteAcceptor" deviceId="1">
<noteAcceptorStatus configurationId="..."
noteValueInEscrow="0"/>
</statusInfo>
</deviceList>
...
</eventReport>
Actually noteValueInEscrow is omitted because the default is 0

## Slide 75: transactionList Element
transactionList contains 1 or more transactionInfo elements
  transactionInfo has the attributes: deviceClass, deviceId
  transactionInfo has 1 sub-element: [device log], which is the log element of the affected device
<eventReport ... transactionId="888">
<transactionList>
<transactionInfo deviceClass="G2S_noteAcceptor" deviceId="1">
<notesAcceptedLog ...
currencyId="USD" denomId="500000"
noteDateTime="..." transactionId="888" />
</transactionInfo>
</transactionList>
...
</eventReport>

## Slide 76: meterList Element
meterList contains 1 or more meterInfo elements
  meterInfo is the element used in meter inquiry, but has meterInfoType="G2S_onEvent"
  deviceClass, deviceId are contained within the device meter sub-element
<eventReport ... transactionId="888">
...
<meterList>
<meterInfo meterDateTime="..." meterInfoType="G2S_onEvent" >
<deviceMeters deviceClass="G2S_noteAcceptor" deviceId="1">
<simpleMeter meterName="G2S_currencyInAmt"
meterValue="2500000"/>
...
</deviceMeters>
</meterInfo> ...
</meterList>
</eventReport>

## Slide 77: Lab 3-3
Inspect data associated with Cabinet events
  eventHandler.eventReport command
  E.g. Door open, affected status and meters
Check eventHandler commands used in host startup algo.
Event subscription management:
  Read subscription of cabinet event
  Clear the subscription
  Set subscription to CBE303, CBE304. Don't send any affected data.
  Trigger events. Any affected data in events?
  Set subscription again, but add affected data. Any affected data in events?
  Set subscription again, but don't send affected data. How are the subscription combined with 'OR'?

## Slide 78: Part D. Connection monitoring and event buffering
How an EGM monitors the health of its connection with host, and importance of buffering of significant events in case of network outage

## Slide 79: Outline
Transport monitoring
  Comms device monitors whether messages can be exchanged between EGM and host
  If transport is down, EGM may need to disable itself
Persisted events
  Resending events and event log
    Request and response
    log access commands
  eventHandler status and profile
  If the event log is full, EGM may need to disable itself

## Slide 80: Status and profile of Comms
Comms device monitors the transport state between the EGM and the owner host.
  Device status indicates the current transport status
  Device profile configures the monitoring policy
<communications deviceId="1" sessionType="G2S_response" ... >
<commsProfile requiredForPlay="true" noResponseTimer="30000"
timeToLive="30000" allowMulticast="true" ... />
</communications>
<communications deviceId="1" sessionType="G2S_response" ... >
<commsStatus transportState="G2S_transportUp" inboundOverflow="false" outboundOverflow="false"
hostEnabled="true" egmEnabled="true" commsState="G2S_onLine"... />
</communications>

## Slide 81: Disable EGM when host unreachable
  The status attribute transportState of the comms device reports the current state of the transport between the EGM and the owner host.
    Common values: G2S_transportUp, G2S_hostUnreachable
    Related events: CME120 Comms Host Unreachable
Comms device detects the host-unreachable condition in two ways:
  the underlying transport, e.g. when the EGM cannot open an HTTP connection to the web service at host.
  the EGM receives no message from host for a long time.
Some jurisdiction requires to disable an EGM when transportState=G2S_hostUnreachable. This can be enforced by setting the profile attribute requiredForPlay=true
  The EGM is disabled with egmState=G2S_transportDisabled
  The association is closed and restarted
This lost communication detection mechanism doesn’t work in SmartEGM.

## Slide 82: Heart beats
If EGM receives no message within the noResponseTimer period, a host-unreachable condition is reported.
  Probably transport is down, or host is overloaded.
... however …
When there are not player activity, the EGM is idle and may not send messages to a host for a long time.
Solution: EGM and host may send heart beat message keepAlive to each other. The receiver must respond with keepAliveAck.
keepAlive
keepAliveAck
keepAlive
keepAliveAck

## Slide 83: Setting the heart beat frequency
At the end of host startup algorithm, a host typically requests the EGM to send keepAlive periodically when the association is idle.
Host sends setKeepAlive with attribute interval, which sets the heart beat frequency in milliseconds. Zero disables the keepAlive timer.
setKeepAlive interval=30s
setKeepAliveAck
keepAliveAck
keepAlive
keepAliveAck
keepAlive
Every 30s, the EGM sends a keepAlive message to host.

## Slide 84: Buffering of events
“If unable to communicate the required information to the MCS, the interface element must provide a means to preserve all mandatory meter and significant event information until such time as it can be communicated to the MCS. Gaming Device operation may continue until critical data will be overwritten and lost.” … from GLI-13 2.1.4
Questions:
  How the EGM knows that the host has received and processed an event?
  How eventHandler device provides event buffering that supports resending events?
  Does event buffering work in case of power outage?
  How to disable EGM when the event buffer is full and so cannot keep critical event information?

## Slide 85: Resending a persisted event
EGM adds an persisted event to event log when it sends eventReport.
After a host processes eventReport requests, it must return eventAck to EGM.
  If EGM does not receive the ack after a timeout period, it resends the event
  EGM will reconstruct a command from the event log, collect associated data and submit the new command to comms device.
The EGM also retries unacknowledged eventReport at EGM restart.
eventReport
eventAck
eventReport
eventReport
eventReport
eventAck
Notes: The event log keeps track of whether the events are acknowledged. The EGM will retry sending commands for events not acknowledged by hosts.

## Slide 86: Event log
Each eventHandler device uses an event log to keep track of persisted events.
  Each entry is identified with a logSequence number
  The attribute eventAck indicates whether the event was acknowledged
  If the event log is full, the status attribute eventHandlerOverflow becomes true.
Log sequence | Transaction ID | Device class and ID | Event code | Event ID | Event DateTime | eventAck | …
899 | 0 | Cabinet 123 | CBE203 | 1061 | .. | false | …
898 | 0 | Cabinet 123 | CBE001 | 1060 | .. | true | …
897 | 0 | Cabinet 123 | CBE303 | 1059 | .. | true | …
… | … | … |  |  | … |  | 
868 | 0 | Comms 1 | CME100 | 1003 | .. | true | …
867 | 0 | Comms 1 | CME002 | 1002 | .. | true | …
866 | 0 | Comms 1 | CME121 | 1001 | .. | true | …

## Slide 87: Accessing Event Log
Two pairs of commands to read log entries:
  getEventHandlerLogStatus / eventHandlerLogStatus gets the lastSequence and totalEntries
  A host sends getEventHandlerLog to retrieve totalEntries entries from the log. The latest entries obtained has logSequence=lastSequence
  EGM returns eventHandlerLogList
Similar commands to access other G2S transaction logs
getEventHandlerLogStatus
eventHandlerLogStatus
getEventHandlerLog
eventHandlerLogList
get[Class]Log for { eventHandler, optionChange, progressive, bonus, voucher, handpay, wat, player } , gamePlay.getRecallLog, getNotesAccepted

## Slide 88: Event Log Entry
EGM returns eventHandlerLogList, which contains some eventHandlerLog elements
  logSequence: unique log sequence number
  deviceClass, deviceId: device that generates the event
  eventCode, eventText, eventDateTime
  eventId: unique identifier for the event
  eventAck: indicates whether the event has been acknowledged
  transactionId: id of the initiating transaction

## Slide 89: Affected data and Event Log Entry
No affected data is saved in log!
But the log may contain sub-elements affectedDeviceList, affectedTransactionList, affectedMeterList to record which data sets are affected.
When eventReport is generated or retried, EGM gathers affected data and adds them to the eventReport message. This is then saved to the message outbound queue.
  Data values may differ from the values at the event trigger moment!
Note: SmartEGM does not save the lists of affected data in event handler log…

## Slide 90: Overflow of event log
If an EGM loses communication with a host, or if the host is overloaded and does not return responses promptly, unacknowledged events accumulate in the event log.
When the event log overflows,
  Cannot persist new event without overwriting old log entry.
  Should the EGM discard new event, or overwrite old event log entry?
  Should the eventHandler device disable the EGM and stop game play?

## Slide 91: Status and profile of eventHandler
Device status indicates the current state of the event queue
Device profile configures how to handle overflow of event queue. (disable EGM? overwrite old event / discard new event?)
<eventHandler deviceId="1" sessionType="G2S_response" ... >
<eventHandlerProfile requiredForPlay="true"
minLogEntries="35" timeToLive="30000"
queueBehavior="G2S_disable" g2s1:disableBehavior=“G2S_overwrite" ... />
</eventHandler>
<eventHandler deviceId="1" sessionType="G2S_response" ... >
<eventHandlerStatus hostEnabled="true" egmEnabled="true" eventHandlerOverflow="false" … />
</eventHandler>

## Slide 92: Event Handler Status
A host uses setEventHandlerState (with attribute enable) to enable / disable the eventHandler device. The host reads status with getEventHandlerStatus
The response eventHandlerStatus has attributes
  hostEnabled: when disabled, egm
    must not generate any eventReport
    must not persist any event for host subscription
    may persist events from forced subscription, and report the events to the host when the device is re-enabled.
  egmEnabled: may be disabled when event queue is full
  eventHandlerOverflow indicates whether the event handler queue is full.
The host may disable the eventHandler device temporarily while it is not ready to process events.

## Slide 93: eventHandler Profile
Host retrieves the profile by getEventHandlerProfile / eventHandlerProfile
Some eventHandlerProfile attributes:
  queueBehavior: behavior when event queue is full.
    G2S_disable: disable the device
    G2S_discard: discard the event
    G2S_overwrite: discard the oldest event in log
  g2s1:disableBehavior: behavior when event queue is full and the device is disabled by EGM. (G2S_discard or G2S_overwrite)
  timeToLive: TTL value for eventReport
eventHandlerProfile has sub-elements forcedSubscription

## Slide 94: eventHandler configuration
queueBehavior | disableBehavior | When overflow ..
discard |  | discard new event
overwrite |  | discard the oldest event in log
disable | discard | Discard new event AND set egmEnabled=false
disable | overwrite | Discard the oldest event in log AND set egmEnabled=false
In the 3rd and 4th cases, eventHandler device is disabled by EGM when event log overflows.
If, in addition, the eventHandler device has profile attribute requireForPlay=true, the EGM is disabled
  egmState = egmDisabled

## Slide 95: Some eventHandler Events
Event Code | Description
G2S_EHE001 | Device disabled by EGM
G2S_EHE002 | Device not disabled by EGM
G2S_EHE003 | Device disabled by host
G2S_EHE004 | Device not disabled by host
G2S_EHE101 | Event subscription changed
G2S_EHE102 | Event handler queue overflow
G2S_EHE103 | Event handler queue overflow cleared

## Slide 96: Lab 3-4
Keep alive
  Turn off the keep alive heartbeat
  Send command to disable the comms device. Are they any communications between EGM and host?
Persisted event
  clear event sub in Cabinet device, then add non-persisted event sub
  Verify that non-persistent events are sent as 'Notification' instead of 'Request'
  Inspect the event log by getEventHandlerLog (note: RST does not save affected* in log).
Event subscription persisted
  Clear event subscription, restart EGM, check transcript for comms event.
  Repeat above, but shutdown RST and start again. concl. RST persists EGM configuration in shutdown

## Slide 97: Note about restart RST
Event subscription persisted
  Clear event subscription, restart EGM, check transcript for comms event.
  Repeat above, but shutdown RST and start again. concl. RST persists EGM configuration in shutdown
  Unload and load SmartEGM config: clear meters and logs

## Slide 98: Note about restarting, 2
Restart EGM: device reset, device changed, subscription lost = false. Meter reset=true
  Persist event sub & log
  BUT Persist meters. meters are NOT reset
Shutdown RST, restart EGM: same flags as above
  Persist meters & event sub. Clear log
Reload EGM config. Start EGM: device reset, device changed, subscription lost, meter reset = true
  Clear meters and log and event sub